ECE1387 – Assignment 1 – FPGA Maze Routing
Kevin Murray – 996088175
October 12th, 2012

File locations
Executable: /autofs/seth.eecg/nfs.eecg.homes.extgrad/kmurray/ece1387/assignment1/kroute
Source: /autofs/seth.eecg/nfs.eecg.homes.extgrad/kmurray/ece1387/assignment1/SRC

Instructions on running
To run routability driven router only:
$ ./kroute -c <circuit_name>

To turn on interactive graphics::
$ ./kroute -c <circuit_name> --interactive_graphics

To turn on reservoir optimization:
$ ./kroute -c <circuit_name> --opt_reservoirs

Also see:
$ ./kroute –help

Benchmark Results

Benchmark	Total # Segs	Default Phi	Optimized Phi	Min W
fcct1_12	63	48.3	46.5 (-4%)	4
fcct2_12	414	336	302.5 (-10%)	6
fcct3_12	4328	3758.6	N/A*	22
fcct4_12	10977	9597.9	N/A*	30

* Did not route successfullly in 1 minute with reservoir optimizations

Flow Description

The implimented router is based around the Pathfinder negotiated congestion algorithm. It consists of a cost drivn maze router (Lee's algorithm) used to route individual nets, being run inside a larger loop that handles congestion.

The algorithm operates on a routing resource graph generated from the circuit description of grid size and